## Slide 1: Technology Assessement Framework (TAF) for Selected WASH Technologies in Ghana
Eric Antwi Ofosu (PhD)
Smart Sanitation & Washtech - KNUST

## Slide 2: Summary of presentation
Background
Four steps of TAF
1. Screening
2. Assessment
3. Presentation of Results
4. Interpretation

## Slide 3: A Metaphor
Technology Introduction - a Journey of change:
The destination, the way to follow, the actors needed, attitude of actors....
TAF is a decision making tool on the applicability and sustainability of the use of a specific WASH technology in a specific context

## Slide 4: TAF - Key Elements for Technology Introduction
Introduction Process
Investment model
Roles and responsibilities
of actors in introduction
process
- Social Marketing
- Resources
Context /
Enabling Environment
- Physical
- Social
- Economic
- Legal
Institutional
Skills and capacities
Technology/Product
Characteristics/Performance
Requirements
- Development process
ACTORS
User, Buyer
Producer, Provider,
Regulator, Supervisor
….

## Slide 5: Key Phases of technology introduction
Process design depends on investment model selected
The various actors involved have to take on their roles in all phases of the introduction process

## Slide 6: Four Steps in TAF Assessment
The TAF process starts with a screening. The screening focuses on two key questions:
» Is there a need for this technology?
» Is the implementation of this technology feasible in this region at all?
If the screening is positive, the technology is comprehensively assessed in step 2.
In step 3 the results are collected and presented.
In step 4 all results are comprehensively interpreted.
  à  à  à 
Screening Assessment Presentation of Results Interpretation

## Slide 7: Step 1: Screening
Purpose is to reject technologies which are not suitable in the context  efficiency of TAF tool
Screening using 2 criteria:
Screening is based on prepared questionnaires
For each type of technology one questionnaire is prepared, called Screening Sheet
Identification
Context
Need
Applicability
Result:
“Yes” or, “Yes but” or “No” and “comments”
  à  à  à 
Screening Assessment Presentation of Results Interpretation

## Slide 8: Step 2: Assessment
Six dimensions of sustainability:
Economic and Financial
Social
Environmental
Institutional & Legal
Skills & Knowhow
Technological
  à  à  à 
Screening Assessment Presentation of Results Interpretation

## Slide 9: Step 2: Assessment
Perspectives of Key actors:
User or Buyer
Producer or Provider
Regulator, Investor, Supervisor, Facilitator
  à  à  à 
Screening Assessment Presentation of Results Interpretation
Methodology of TAF puts particular emphasis on perspectives and roles of key actors in the introduction process and forces TAF user to consider these perspectives in the assessment of impacts concerning the sustainability dimensions.

## Slide 10: Assessment Indicators
  à  à  à 
Screening Assessment Presentation of Results Interpretation

## Slide 11: Step 2: Assessment
Assessment using the TAF:
Based on 18 indicators : Nr. 1...18
Using questionnaires
For each indicator one set of Assessment Indicator Sheets exist
Assessment Indicator Sheets include
  - General information
  - 3-5 Guiding questions
  - 1 Scoring question
  Each application needs specific planning of data collection
  à  à  à 
Screening Assessment Presentation of Results Interpretation

## Slide 13: Indicator 1

## Slide 14: Step 2: Assessment
Scoring method
To support the scoring additional information and links are provided on indicator sheets
Different views and scoring in a group are common
Different views should be made explicit
Reasons and implications for overall result of assessment should be discussed and documented
Transparent procedure supports acceptance of assessment results
  à  à  à 
Screening Assessment Presentation of Results Interpretation

## Slide 15: Step 3: Presentation of Results
From Step 1: Screening results for criteria “need” and “applicability” and comments
From Step 2: Each score will be presented in a table as presented on the left
Comments from Step 2 are collected on a separate sheet, in particular if conflicting scoring appeared
  à  à  à 
Screening Assessment Presentation of Results Interpretation

## Slide 16: Step 4: Interpretation
Comprehensive interpretation including all these steps:
1) Step 1: Straight forward interpretation of screening results
2) Step 2: Interpretation
Per row  per dimension
Per column per perspective
3) TAF Graphical Profile  comprehensive assessment
4) Comments
  à  à  à 
Screening Assessment Presentation of Results Interpretation
TAF Profile

## Slide 17: Step 4: Interpretation
  à  à  à 
Screening Assessment Presentation of Results Interpretation
The TAF provides a comprehensive basis for decision making
The interpretation of results should consider all elements – from step 1 and from step 2
Implications from conflicting scoring should be made explicit
The process of TAF application supports acceptance of the assessment result and the development of specific mitigation measures for supporting the introduction process
All results and interpretation should be comprehensively documented

## Slide 18: THANK YOU